## Slide 1: Merrimon Information
French Broad River MPO

## Slide 2: General Summary
NCDOT plans to resurface US 25 from Southside Avenue to Midland Drive in 2022
Implementing a road diet from WT Weaver Boulevard to Wembley Drive (current end of the four-lane cross-section) is being considered as part of the resurfacing project
MTP Road Diet Project
Proposed Road Diet Through Resurfacing

## Slide 3: Complete Streets
Initially adopted in 2012 and further refined in 2019:
“The purpose of this policy is to guide existing decision making and design processes to ensure that all users are included during the planning, design, construction, funding, operation and maintenance of North Carolina’s transportation network, and will not create barriers or hazards to the movements of those users.”

## Slide 4: Road Diet Benefits
FHWA Proven Safety Countermeasure
19-47% reduction in total crashes
Reduction of rear-end and left-turn crashes due to the dedicated left-turn lane
Reduced right-angle crashes
Fewer lanes for pedestrians to cross
Opportunity to add bike lanes, parking, additional pedestrian space
More consistent speeds
Typically implemented on roads with 25,000 AADT or less

## Slide 5: Context
Safety
  31 recorded bicycle and pedestrian crashes
  150% crash rate of similar roadway segments
Volumes
NOTE: volumes about 12-18% higher in 2019
  North of WT Weaver (2020)
    11,500-20,000
  South of WT Weaver (2020)
    18,500-21,000

## Slide 6: Context
Several Intersections on Merrimon with safety issues identified in NCDOT HSIP reports between 2017-2021
  Just north of Beaverdam
  Ottari Road
  Maney Avenue
  Edgewood Road
  Westall Drive
  Murdock Avenue
  Coleman Avenue
  Hillside Drive
  Woodrow Avenue
  Merrimon Drive

## Slide 7: Context
Walkable context suggests latent demand
  FBRMPO Congestion Management Process
  EPA Smart Location Database

## Slide 8: Planning Background

## Slide 9: Planning Background
2045 Metropolitan Transportation Plan

## Slide 10: Planning Background
Congestion Management Process

## Slide 11: Planning Background
Two intersection projects funded in P 3.0 were defunded in 2020
Initially proposed five-lane cross-section between WT Weaver and Edgewood on Merrimon
Negative public feedback at meetings in 2018

## Slide 12: Considerations
Can a road diet on Merrimon work without immediate improvements to intersections and other improvements?