## Slide 1: Transportation Design for Wildlife Crossings
Scott Adams, AICP Transportation Planner French Broad River MPO
September 21, 2023

## Slide 2: Who We Are
The MPO & RPO carry out the Federal transportation planning process with local governments, NCDOT, and other partners.
The process is focused on being:
  Comprehensive
  Cooperative
  Continuous
1
Notes: MPO in red, RPO in orange.

## Slide 3: What We Do
Life of a Transportation Project
CTP
30+ Years
No $ Constraint
MTP
25 Years, Used for AQ Determinations
Based on Revenue Forecast
SPOT
Scores Projects for Effectiveness
Results go into STIP/TIP
STIP/TIP
0-5 and 6-10 Years
Specific Funding Sources Identified
Construction
Project Let, Built
NEPA/Design
Project alternatives are assessed
Final project design and cost
2040 Plan
Statewide Vision
Strategic Corridors
State
State
Feds
Feds
State
All phases are important, but these are key.
2
Notes: NCDOT Strategic Prioritization Office of Transportation (SPOT)

## Slide 4: Why Is This Important?
Three main reasons people care about this issue:
  Interest in wildlife conservation
  Concern for human safety
  Economics
“No matter who you are, where you live, or what you do for a living, you’re going to care about at least one of these.” Marcel Huijser, Senior Research Ecologist Western Transportation Institute Montana State University (Bozeman) 20 years of road ecology studies
NCDOT Complete Streets Policy
“Routine Accommodation” can occur via:
  Resurfacing
  Maintenance
  New construction
3
Additional framework for
Routine Accommodation
Notes: NCDOT Complete Streets
Policy Exceptions
Unique site constraints
Distance from existing/planned facilities
Bike/Peds prohibited
No existing/planned transit service
Evaluated by Complete Streets Review Team
Policy Exceptions
Unique site constraints
Distance from existing/planned facilities
Bike/Peds prohibited
No existing/planned transit service
Evaluated by Complete Streets Review Team

## Slide 5: Definitions
Notes from Ron Sutherland, Chief Scientist, Wildlands Network
“A wildlife corridor is the term we use for a defined movement pathway that, if protected or restored, would provide essential habitat connectivity for one or more species,” he says.
“A wildlife road crossing, on the other hand, is “a structure that is designed to allow wildlife to safely cross over or under a busy road,” he says.
4
Notes: Stecoah Gap Overpass, on NC 143, just west of Andrews, NC

## Slide 6: Why Now?
The Numbers:
  Wildlife Vehicle Crash (WVCs) impacts to wildlife and humans alike via injuries and deaths.
  WVCs are costly, and preventative measures are a good investment.
  There’s money available to address the issue via the IIJA/BIL’s Wildlife Crossings Pilot Program (WCPP).
5
Notes: The Bipartisan Infrastructure Law, as enacted in the Infrastructure Investment and Jobs Act,

## Slide 7
6
Source: Animal Road Crossing (ARC),
https://arc-solutions.org/wp-content/uploads/2021/11/Wildlife-Crossings-Pilot-Program-Summary.pdf

## Slide 8: Roads & Wildlife in USA
7
Source: Animal Road Crossing (ARC),
https://arc-solutions.org/wp-content/uploads/2021/11/ARC-CLLC-Roads-Infographic.pdf

## Slide 9: Roads & Wildlife in NC
2017-2019
56,868 wildlife-vehicle collisions (WVCs)
$156.9 million in property damage
2,800+ human injuries
5 human fatalities
Source: NCDOT Transportation & Safety Division Study – June 2020
8

## Slide 10: Recent NC Studies
9

## Slide 11: Pigeon River Gorge Study
Study identified 20 sites:
  13 sites in NC (4 High-Priority sites)
  7 sites in TN (3 High-Priority sites)
NOTE: 120 cameras over 28 miles (I-40 Pigeon River Gorge Wildlife Crossing Project)
10

## Slide 12: NC Statewide Study
On road segments with 5 deer-vehicle collisions or 2 elk-vehicle collisions per mile per year, the cost of collisions exceed the cost of wildlife crossing structures, notably Deflection Fencing.
  Avg. deer-vehicle collision cost: $6,000
  Avg. elk-vehicle collision cost: $17,000
The statewide study identified 155 wildlife crossing priority sites across NC, including Top 20 Sites. (5 in Land of Sky region)
11
Notes: Source: pg. 7, of report cited on-screen
“Collision-related costs add up to roughly $12 billion annually in the U.S.,” he says. “The cost of a deer–vehicle collision averages around $6,000 and running into an elk can cost upwards of $17,000.”
Wildlife crossing structures and road mitigation have improved human safety and wildlife corridor connectivity at Snoqualmie Pass on I-90 in Washington State, along the Trans-Canada Highway in the Rocky Mountains and Banff National Park, and on the Flathead Indian Reservation in Western Montana where Huijser worked for 13 years. In these examples, fencing successfully reduces collisions and guides wildlife to safe-crossing opportunities such as vegetated overpasses, open-span bridges, and large- and medium-mammal underpasses. Dozens of such wildlife corridor projects have led to an 80–95 percent collision reduction with large mammals like deer and elk since the mid-’90s.

## Slide 13: Types of Crossings
Signs (static)
Interactive Signs
Round Culverts
Box Culverts
Multi-Plate Arches
Open-Span Bridges
Bridge Extensions
Wildlife Underpasses/Overpasses
Ideally, a combination of various crossing types—like a buffet of choices—should be provided, spaced out in such a way that animals do not need to travel great distances to find a crossing opportunity.
Photo by Marcel Huijser
12
Deflection
Fencing
Notes: Source: text and photos from https://appvoices.org/2021/03/18/i40-wildlife-connectivity/
Although road mitigation measures are good for human safety and for animals, they cost money. Fences may cost about $100,000 per mile, an underpass may require around half a million to build, and a single wildlife overpass can cost up to $10 million.

## Slide 14: Signs
13
US 191 in Yellowstone N.P.

## Slide 15: Signs
Perception-reaction time is key.
14
Notes: The Netherlands is slightly larger than the state of Maryland.

## Slide 16: Signs/Fencing example, US 64 at Panther Mtn.
15
Wildlife travel path
Deflection Fencing

## Slide 17: Underpasses
NOTE: Natural-bottomed culverts are more effective at supporting aquatic species
16

## Slide 18: Bridges & Overpasses
NOTE: Daylight and natural vegetation-screening are key to increasing wildlife’s degree of comfort with constructed structures; if an animal cannot see daylight, they may feel confined or like the structure’s a trap.
17

## Slide 19: Bridges & Overpasses
NOTE: Structures can be designed to achieve multi-functionality – i.e. wildlife crossing and hydrology, etc.
18

## Slide 20: Not Just Big Critters
19
Source: Wildlands Network
https://wildlandsnetwork.org/news/monitoring-crossing-structures-reveals-timber-rattlesnakes
Notes: https://wildlandsnetwork.org/news/monitoring-crossing-structures-reveals-timber-rattlesnakes

## Slide 21: So What Works?
Chart: % Reduction in Collisions
| Reflectors | Whistles | Standard Signs | Seasonal Warning Signs | Fencing + Under/Overpasses
 | 0.015 | 0.015 | 0.015 | 0.26 | 0.97
20
Source: Animal Road Crossing (ARC),
https://arc-solutions.org/wp-content/uploads/2021/11/ARC-CLLC-Roads-Infographic.pdf

## Slide 22: The Details
21

## Slide 23: The Details
22

## Slide 24: The Details
23

## Slide 25: The Details
24
TRIPLE 8'X11'RCBC;439’
ALONG CENTERLINE CULVERT
SINGLE 18'X14' VEHICULAR UNDERPASS;
127' ALONG CENTERLINE
TRIPLE 12'X13' RCBC;
101' ALONG CENTERLINE CULVERT

## Slide 26: The Details
24
9/21/23, Steve Goodman, NPCA:
Remove the concrete ditch swale on one or both sides and truncate the abutment slope by introducing a vertical retaining wall just in front of the piers. Consider standalone combined wildlife and AT structure.

## Slide 27: The Details
24
9/21/23, Steve Goodman, NPCA:
Wolf Laurel Exit Bridge: Truncate the abutment slope by introducing a vertical retaining wall just in front of the piers. Big Laurel Bridge: add level bench paths.
Big Laurel Bridge
Wolf Laurel Exit Bridge
Big Laurel Bridge
Wolf Laurel Exit Bridge

## Slide 28: NCDOT – Stecoah Gap Overpass
25

## Slide 29
Thank You!